## Slide 1: Location, location, location Border effects in interference limited ad hoc networks
Orestis Georgiou
Shanshan Wang, Mohammud Z. Bocus
Carl P. Dettmann
Justin P. Coon
MoN14
21 September 2015
CNET-ICT-318177

## Slide 2: Motivation
IoT and WSNs
  Temperature, pressure, humidity, etc.
  Smart cities, smart buildings
  e-Health
Co-channel Interference
  Packet losses
    Retransmissions
    Delays
    Energy waste
  Overheads

## Slide 3: Motivation for Theoretical approach
SINR model to design efficient MAC
  Statistical framework
    Network performance: Local / Global observables
  Randomness (is good):
    Multipath (fast fading)
    Shadowing (slow fading)
    Number and Location of wireless devices
      Ad hoc, mesh net, mobile, physical constraints and costs
    Power control
      Cooperation or signalling overheads
    MAC
      ALOHA / CSMA
(Poisson) Point Process (with no carrier sensing)
  “Poissonian Network” a theoretical abstraction (a playground)

## Slide 4: Motivation & Contributions
Different locations of a receiver
The desired transmitter is at a constant distance from the receiver
Concurrent transmitters are uniformly distributed
Topological inequalities in the network
Channel access unfairness in 802.11 where nodes at the border are typically favoured

## Slide 5: Motivation & Contributions
Different locations of a receiver
The desired transmitter is at a constant distance from the receiver
Concurrent transmitters are uniformly distributed
Topological inequalities in the network
Channel access unfairness in 802.11 where nodes at the border are typically favoured

## Slide 6: Motivation & Contributions
1
1/2
1/4
1/4
1/2
1
Interference experienced by a receiver is strongly dependent on its location within a finite network.
The location of the receiver is of equal importance as the total number of concurrent transmitting devices.
Contributions
  Closed form expressions for:
  Outage probability
  Achievable ergodic rate
  Spatial density of successful transmissions
Location, location, location: Border effects in interference limited ad hoc networks, OG et. al. WiOpt'15 (2015).

## Slide 7: Model definitions
PPP (no carrier sensing)
Path loss function
Rayleigh fading
SINR at receiver
Path loss attenuation function
Path loss exponent
Channel gain
Interference factor

## Slide 8: Model definitions
PPP (no carrier sensing)
Path loss function
Rayleigh fading
SINR at receiver

## Slide 9: Coverage - standard approach
Connection probability
Connection probability
conditioned on the
received interference at j
Laplace transform of the r.v.
Ij evaluated at s
conditioned on the
locations of nodes ti and rj
J. G. Andrews et al, “A tractable approach to coverage and rate in cellular networks,” 2011

## Slide 10: Coverage - infinite Nets
The probability generating function for a general inhomogeneous PPP
Olbers’ dark night sky paradox (1823)
Requires that

## Slide 11: Coverage - infinite Nets
Why is the night sky dark?
Kepler 1610
Why is the night sky dark?
Kepler 1610

## Slide 12: Coverage - from infinite to finite Nets
The probability generating function for a general inhomogeneous PPP

## Slide 13: Coverage - from infinite to finite Nets
Topological inequalities in the network
Channel access unfairness in 802.11 and 802.15.4 where nodes at the border are typically favoured.
Routing, MAC, retransmission schemes can be smarter i.e. location and interference aware

## Slide 14: Coverage - from infinite to finite Nets
Location, location, location: Border effects in interference limited ad hoc networks, OG et. al. WiOpt'15 (2015).

## Slide 15: Coverage - from infinite to finite Nets
Location, location, location: Border effects in interference limited ad hoc networks, OG et. al. WiOpt'15 (2015).

## Slide 16: Capacity - from infinite to finite Nets
Location, location, location: Border effects in interference limited ad hoc networks, OG et. al. WiOpt'15 (2015).

## Slide 17: Spatial density of successful transmissions
How many signals can the receiver rj decode successfully?

## Slide 18: Discussion and Summary
The location of the receiver is equally important to the total number of concurrent interfering transmissions
Location, location, location
Routing, MAC, retransmission schemes can be smarter
  i.e. location and interference aware.
Location, location, location: Border effects in interference limited ad hoc networks, OG et. al. WiOpt'15 (2015).

## Slide 19: Motivation & Contributions
Topological inequalities in the network
Channel access unfairness in 802.11 where nodes at the border are typically favoured
Thank you for your attention!